## Slide 1: Pill Reminder V2
Design Concept

## Slide 2
Pill Carousel
TOP
SIDE
BOTTOM
Alignment Pegs
Closed
Open

## Slide 3
TOP COVER
Open Slot (exposes a pill slot or a closed slot on the carousel, depending upon the time).
Closed Cover
Carousel rotates under the cover

## Slide 4
PLATEN
TOP
SIDE
GearMotor (30 - 60 rpm)
Optocoupler
Index holes centered on pill slots
Holes for carousel
Alignment pegs
Raised mount for carousel
Platen base
Carousel slots into Platen; Platen rotates the carousel via the gearmotor

## Slide 5
Intent is to prevent user from taking pills at the wrong time
  User can only access pills through a slot at the top
  Carousel rotates under the top cover to either expose the correct pill slot or else expose the closest of the 4 closed slots, depending upon the pre-set times of day for pill taking.
Removable Carousel Trays
  For preparing refills offline
  Carousel can only insert into Platen one way
  Platen home position calibrated via a mark on the platen and a setup mode on the app
  Platen slot exposure traced via opto-coupler and the index holes in the platen.
Design Notes

## Slide 6
Design based upon Particle device (Photon or Argon or Photon 2)
App is provided
  App used for initial position calibration
  App has a screen for setting # pill taking times per day and the time window for each
Enclosure houses 16x2 LCD display, red and green LEDs, PIR and (optionally) a piezo buzzer.
  Carousel moves to proper position during a pill taking time, when the PIR is activated (motion detected near the device)
  Carousel moves to nearest closed slot when the current pill taking time ends.
  Red LED lights (flashes) when carousel is moving.
  Green LED lights (flashes) when pills are under the cover slot and available for taking
  LCD displays local date/time or messages (pill refill needed, carousel moving, etc.)
Design Notes (2)

## Slide 7
Mechanical Calibration: If the Particle device reboots, how does it know where the platen is?
    Solution #1: There is an initial mechanical (manual) calibration when the unit if first assembled. Thereafter, the Particle device maintains knowledge and tracking of platen position via non-volatile RAM. Position tracking thereafter will be valid until the unit is disassembled and reassembled.
    Solution #2: Add another index hole or slot at the outside edge of the platen and another opto-isolator to detect it. Now, the Particle device firmware can be used to automatically calibrate each time the device is re-booted and the carousel position tracked using regular volatile RAM.
Issues